## Slide 1: Lecture 2 Camera Models
Lecture 2 -
Silvio Savarese
10-Jan-18
Professor Silvio Savarese
Computational Vision and Geometry Lab

## Slide 2: Lecture 2 Camera Models
Lecture 2 -
Silvio Savarese
10-Jan-18
Pinhole cameras
Cameras & lenses
The geometry of pinhole cameras
Reading:
[FP] Chapter 1, “Geometric Camera Models” [HZ] Chapter 6 “Camera Models”
Some slides in this lecture are courtesy to Profs. J. Ponce, S. Seitz, F-F Li

## Slide 3: How do we see the world?
Let’s design a camera
  Idea 1: put a piece of film in front of an object
  Do we get a reasonable image?

## Slide 4: Pinhole camera
Add a barrier to block off most of the rays
  This reduces blurring
  The opening known as the aperture
Apertur e

## Slide 5: Some history…
Milestones:
Leonardo da Vinci (1452-1519):
first record of camera obscura (1502)

## Slide 6: Some history…
Milestones:
Leonardo da Vinci (1452-1519): first record of camera obscura
Johann Zahn (1685): first portable camera

## Slide 7: Some history…
Milestones:
Leonardo da Vinci (1452-1519): first record of camera obscura
Johann Zahn (1685): first portable camera
Joseph Nicéphore Niépce (1822): first photo - birth of photography
Photography (Niépce, “La Table Servie,” 1822)

## Slide 8: Some history…
Photography (Niépce, “La Table Servie,” 1822)
Milestones:
Leonardo da Vinci (1452-1519): first record of camera obscura
Johann Zahn (1685): first portable camera
Joseph Nicéphore Niépce (1822): first photo - birth of photography
Daguerréotypes (1839)
Photographic Film (Eastman, 1889)
Cinema (Lumière Brothers, 1895)
Color Photography (Lumière Brothers, 1908)

## Slide 9: Let’s also not forget…
Aristotle (384-322 BC)
Also: Plato, Euclid
Al-Kindi (c. 801–873)
Ibn al-Haitham (965-1040)
Motzu (468-376 BC)
Oldest existent book on geometry in China

## Slide 10: Pinhole camera
f = focal length
o = aperture = pinhole = center of the camera
f
o

## Slide 11: Pinhole camera
Derived using similar triangles
[Eq. 1]
f

## Slide 12: Pinhole camera
i
O
f
k
[Eq. 2]
f

## Slide 13: Pinhole camera
Kate lazuka ©
Is the size of the aperture important?

## Slide 14: Shrinking aperture size
Adding lenses!
-What happens if the aperture is too small?
-Less light passes through

## Slide 15: Cameras & Lenses
A lens focuses light onto the film
image
P
P’

## Slide 16: Cameras & Lenses
image
P
Out of focus
P’
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
  Related to the concept of depth of field

## Slide 17: Cameras & Lenses
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
  Related to the concept of depth of field

## Slide 18: Cameras & Lenses
focal point
f
A lens focuses light onto the film
  All rays parallel to the optical (or principal) axis converge to one point (the focal point) on a plane located at the focal length f from the center of the lens.
  Rays passing through the center are not deviated

## Slide 19: Paraxial refraction model
f
zo
-z
From Snell’s law:
[Eq. 3]
[Eq. 4]

## Slide 20: Issues with lenses: Radial Distortion
Pin cushion
Barrel (fisheye lens)
– Deviations are most noticeable for rays that pass through the edge of the lens
No distortion
Image magnification decreases with distance from the optical axis

## Slide 21: Lecture 2 Camera Models
Lecture 2 -
Silvio Savarese
10-Jan-18
Pinhole cameras
Cameras & lenses
The geometry of pinhole cameras
  Intrinsic
  Extrinsic

## Slide 22: Pinhole camera
f = focal length
o = center of the camera
f
[Eq. 1]
->P’=

## Slide 23: From retina plane to images
Pixels, bottom-left coordinate systems
f
Retina plane
Digital image

## Slide 24: Coordinate systems
f
x
y
xc
yc
C’’=[cx, cy]
1. Off set
[Eq. 5]

## Slide 25: Converting to pixels
Off set
From metric to pixels
x
y
xc
yc
C=[cx, cy]
Units: k,l : pixel/m f : m
Non-square pixels
 ,  : pixel
f
[Eq. 6]



## Slide 26: Is this projective transformation linear?
x
y
xc
yc
C=[cx, cy]
f
[Eq. 7]
Is this a linear transformation?
No — division by z is nonlinear
Can we express it in a matrix form?

## Slide 27: Homogeneous coordinates
homogeneous image coordinates
homogeneous scene coordinates
EàH
Converting back from homogeneous coordinates
HàE

## Slide 28: Projective transformation in the homogenous coordinate system
[Eq.8]
Homogenous
Euclidian
Ph
==

## Slide 29: The Camera Matrix
Camera matrix K
f
[Eq.9]
=K

## Slide 30: Camera Skewness
y
xc
yc
C=[cx, cy] x

How many degree does K have? 5 degrees of freedom!
f

## Slide 31: Canonical Projective Transformation
P '  M P
[Eq.10]
M
=

## Slide 32: Lecture 2 Camera Models
Lecture 2 -
Silvio Savarese
10-Jan-18
Pinhole cameras
Cameras & lenses
The geometry of pinhole cameras
  Intrinsic
  Extrinsic
Other camera models

## Slide 33: World reference system
kw
Ow
iw
jw
R,T
The mapping so far is defined within the camera reference system
What if an object is represented in the world reference system?
Need to introduce an additional mapping from world ref system to camera ref system
f

## Slide 34: 3D Rotation of Points
Rotation around the coordinate axes, counter-clockwise:
p
x
Y’
p’

x’
y
z
A rotation matrix in 3D has 3 degree of freedom

## Slide 35: 2D Translation
P
P'
t
Please refer to CA session on transformations for more details

## Slide 36: 2D Translation Equation
P
x
tx
ty
y
P’
t

## Slide 37: 2D Translation using Homogeneous Coordinates
P’
P
x
tx
ty
y
t

## Slide 38: Scaling
P
P'

## Slide 39: Scaling Equation
P
y
P’
sy y
x sx x
S

## Slide 40: Rotation
P
P'

## Slide 41: Rotation Equations
Counter-clockwise rotation by an angle 𝜃
P
P’

x’ x
y’
y
How many degrees of freedom? 1

## Slide 42: Scale + Rotation + Translation
If sx = sy, this is a similarity transformation

## Slide 43: 3D Rotation of Points
Rotation around the coordinate axes, counter-clockwise:
P
x
y’
P’
x’
y
z
A rotation matrix in 3D has 3 degrees of freedom
R  Rx ( ) Ry ( ) Rz ( )

## Slide 44: 3D Translation of Points
A translation vector in 3D has 3 degrees of freedom
P
x Tx
Ty
y
P’
T
z

## Slide 45: 3D Translation and Rotation
x
y z
R  R ( ) R ( ) R ( )

## Slide 46: World reference system
Pw
In 4D homogeneous coordinates: P 
Internal parameters
External parameters
M
iw
kw
Ow
jw
R,T
P
P’
f
[Eq.11]

## Slide 47: The projective transformation
How many degrees of freedom?
5 + 3 + 3 =11!
iw
kw
Ow
jw
R,T
P
P’
f

## Slide 48: The projective transformation
iw
kw
Ow
jw
R,T
P
P’
f
[Eq.12]

## Slide 49: Theorem (Faugeras, 1993)
[Eq.13]

## Slide 50: Properties of projective transformations
Points project to points
Lines project to lines
Distant objects look smaller

## Slide 51: Properties of Projection
Angles are not preserved
Parallel lines meet!
Parallel lines in the world intersect in the image at a “vanishing point”

## Slide 52: Horizon line (vanishing line)

## Slide 53: One-point perspective
Masaccio, Trinity, Santa Maria Novella, Florence, 1425-28
Credit slide S. Lazebnik

## Slide 54
Next lecture
How to calibrate a camera?

## Slide 55: Supplemental material

## Slide 56: Thin Lenses
Snell’s law:
n1 sin 1 = n2 sin 
2
zo
Focal length
[FP] sec 1.1, page 8.

## Slide 57: Horizon line (vanishing line)
horizon
l